## Slide 1: Tips to Reduce AT Value
FIR
  Mirror FIR architecture can save a lot of multipliers
  Be careful when transposed form FIR is used
    Non-transposed form with pipeline also has good result
FFT
  Pipelined architecture (e.g. R2SDF or R22SDF)
  Alpha max plus beta min algorithm
  CORDIC-based architecture
Frequency analysis
  Sequential processing (bubble sorting)
Control circuit
  If possible, avoid using counters in your design
  Use enable flag with FIFO instead

## Slide 2: Tips to Reduce AT Value
General
  Fixed-point analysis on each stage to minimize bit-width
  Use DesignWare to help Design Compiler infer your design more
    e.g. summation and pipelined multiplier
In physical design stage
  Manual floorplan of each block